## Slide 1: CanberraUAV Workshop Communications links
Feb 2017

## Slide 2: Communications
The ability to:
  Receive timely telemetry
  Reliably command the UAV
Includes RC controllers and GCS computers
For safety, a UAV must be able to be commanded at any time

## Slide 3: Communications
There are many types of communications
  Mavlink is independent of the communications hardware
Will skip over RC controllers
  Simple, direct manual control of the UAV
  Range limit of ~500m
  Limit is more the pilot’s eyesight rather than the radio range

## Slide 4: Communications
Link budget tells us the expected range from a given output power (and vice-versa)
  EIRP = Effective Isotropic Radiated Power (power out of antenna)
  FSL = free space loss
  Radio output (Pout) + Antenna gain G(TX) = EIRP
  Pout + G(TX) - FSL >= G(RX) + P(thres)
  P(thres) is the radio sensitivity. Depends on modulation and datarate
Note all units in dB or dWB

## Slide 5: Communications
Antennas
Low gain, non-directional
High gain, directional

## Slide 6: Comms - Point-to-point RF links
Simple serial->RF radios
Typically 57600 baud
Operate on the 915-928 Mhz band (in AUS)
20km+ range, limited by line of sight

## Slide 7: Comms - 3G/4G modems
High bandwidth
Unlimited range*
  (as long as you’ve got network coverage)
Can be difficult setting up a network
  No public IP’s 

## Slide 8: Comms - Long Range Wifi
High bandwidth
5km range with good antennas
Complete control of link

## Slide 9: Comms - Satellite
Very, very expensive
Modem/Antenna size is an issue
10-20 kbps bandwidth
Coverage depends on provider

## Slide 10: Comms - Bandwidth
How much bandwidth do you need?
  MAVLink typically uses 2-4 kbps
  Live imagery can use a few 100kbps, depending on resolution, compression and frame rate
  SSH/remote links to on-board computers?
What about latency?

## Slide 11: Comms - Redundancy
If the UAV is:
  Carrying valuable equipment
  Going beyond line-of-sight
  Is required to have guaranteed comms
Then
  Backup comms links are required

## Slide 12: Comms - Redundancy
Consider
  What data needs to be prioritised
  Comms link coverage
  How quickly the UAV can go to a backup link
  Independent links based on the same technology, or different technologies?
  Use a second UAV as a comms relay

## Slide 13: Comms - Redundancy
Can be complicated quickly
Complexity has it’s own disadvantages

## Slide 14: Comms - Redundancy

## Slide 15: The End!
Link budgets
Typical types of communications systems
Redundancy